NEC SL1100 (analogue phone) - Quick User Guide

MAKING CALLS:

To make a call to another extension:

- Lift handset or press Speaker key (if available).

- Dial extension number (101,102 etc) or press Direct Station Key (if available).

- Wait for answer or talk if the receiving station is hands free.

- To toggle between voice and ringing on receiving phone dial “1”.

To make an outside call:

- Lift handset or press Speaker key (if available).

- Dial “0”

- Dial telephone number.

To make an outside call using system speed dial

- Lift handset or press Speaker key (if available).

- Dial “#2” for system or “#7” for personal

- Dial speed dial location number (000-899 for system or 0 to 9 for personal)

To make a call using Last Number Redial:

- Lift handset or press Speaker key (if available).

- Dial “#5”

ANSWERING CALLS:

To answer an outside call:

- If ringing at your handset – Lift handset or press Speaker key.

- If not ringing at your handset – Lift handset and dial “*#” or “**” extension number.

PLACING/RETREIVING A CALL ON HOLD

- Whilst on a call press recall button (may also be called “flash”, “hook flash” or just “R”)

- To retrieve call repeat above procedure

TRANSFERRING CALLS:

- Press the recall button (may also be called “flash”, “hook flash” or just “R”)

- Dial the extension number (101,102 etc)

- Announce the call

- Hang up. The call will be transferred.

DO NOT DISTURB (DND):

To activate/deactivate

- Lift handset or press Speaker key (if available).

- Dial “747” followed by

- “1” for DND on incoming calls only

- “2” for DND on intercom calls only

- “3” for DND on both incoming and intercom

- “4” for DND on transferred (Call forwarded) calls

- “0” to cancel DND

PAGING:

To page all extensions:

- Lift handset

- Dial “7011”

- Make announcement then hang up.

CALLING DOOR STATIONS:

To call a door station:

- Lift handset”

- Dial “7021” for door 1 or “7022” for door 2.

- To open the door/gate, press recall key (may be called “flash”, “hook flash” or “R”)