NEC SL1100 - Quick User Guide

MAKING CALLS:

To make a call to another extension:

- Lift handset or press Speaker key.

- Dial extension number (101, 102 etc) or press Direct Station Key if programmed.

- Wait for answer or talk if the receiving station is hands free.

- To toggle between voice and ringing dial “1”.

NB: To program your extension for hands free answer on all intercom calls:

- Press Speaker, dial “721” to turn on or “723” to turn off then press Speaker

To make an outside call:

- Lift handset or press Speaker key.

- Dial “0” or press “Line” key

- Dial telephone number.

NB: If the number is dialed without selecting a line first then the number is previewed. Press a line key within 3 seconds to dial the number in the screen.

To make an outside call using speed dial (see below to program speed dial):

- Press Speed dial key (if programmed) and dial location number (000-900) OR

- Press Selection key second from left below display (below Dir in screen)

- Use Alpha keys to go to first letter of name to be searched

- Press Navigation Key         at bottom right of handset DOWN to go to required name

- Press Line key to dial

- For personal speed dial press Speaker, dial #7 then location number (1 to 0)

To make a call using Last Number Redial:

- Press RIGHT hand side of Navigation Key        at bottom right of handset

- To dial last number, press RIGHT hand side of navigation key again or.

- Press Navigation Key DOWN to review last 10 calls made.

- Press a line key to dial the number in the screen.

ANSWERING CALLS:

To answer an outside call:

- If ringing at your handset – Lift handset or press Speaker key.

- If not ringing at your handset – Lift handset and press the flashing Line key.

To answer a call ringing at another extension:

- Press Speaker key or lift handset

- Dial “*#” or dial “**”then extension number

TRANSFERRING CALLS:

To transfer a call:

Method 1:

- Answer or make a call.

- Press the Transfer key.

- Dial the extension number (101, 102 etc) or press the Direct Station Key if programmed.

- Announce the call (optional).

- Hang up. Call will be transferred.

Method 2:

- Answer or make a call as above.

- Press the Direct Station Key (no need for Hold or Transfer keys).

- Announce the call.

- Hang up and the call will be transferred.

To transfer a call from a cordless phone:

- Press the recall button (may also be called “flash”, “hookflash” or just “R”)

- Dial the extension number (101, 102 etc)

- Announce the call

- Hang up. The call will be transferred.

## NEC SL1100 - Quick User Guide

BACKGROUND MUSIC:

To turn background music on/off (where available):

- Press Speaker key, dial “725” then press Speaker key

DO NOT DISTURB (DND):

To activate/deactivate press DND button then:

- “1” for DND on incoming calls only

- “2” for DND on intercom calls only

- “3” for DND on both incoming and intercom

- “4” for DND on transferred (Call forwarded) calls

- “0” to cancel DND

CALL FORWARDING:

To forward calls to another extension:

- Press Speaker key

- Dial “74” then

- Dial “1” for CFW immediate, “2” for CFW busy, “3” for CFW no answer “4” for CFW busy/no answer, “5” for dual ring, or “6” for follow me.

- Dial “1” to set or “0” to cancel

- Dial the extension number to forward to (200, 201 etc)

- Press Speaker

PAGING:

To page all extensions:

- Lift handset

- Dial “7011”

- Make announcement.

- Press receiver down with hand then hang up.

PROGRAMMING SPEED DIAL NUMBERS:

To program speed dial numbers (system and personal):

- Press Speaker key.

- Dial “753” (755 for personal)

- Dial location bin number (000-900) (1 to 0 for personal)

- Dial the telephone number to be stored (Transfer key for a pause, Recall key for a flash)

- NB: dial 0 before personal entries. DO NOT dial 0 before system entries

- Press Hold key

- Enter name using alpha keys (# to move curser, Clear/Back to backspace, Exit to erase entry).

- Press Hold key

- For more numbers enter location bin number, to end press Speaker key.

PROGRAMMING “ONE TOUCH” KEYS

To program one touch keys to be a direct station or speed dial key:

- Press Speaker key.

- Dial “751”

- Press key to be programmed.

- Dial  “01”

- For a Direct Station key, dial extension number to be stored (101, 102 etc)

- For a speed dial key, dial “0” then telephone number to be stored or “27” followed by speed dial location number

- Press Hold key then Speaker key.

TO CHANGE SYSTEM TIME:

- Press Speaker key

- Dial 728

- Dial time in 24 hour format (eg: 205PM = 1405)

- Press Speaker key

## NEC SL1100 - Quick User Guide

CALL CONFERENCING:

To connect lines and/or extensions in a multi party conference:

- Make a call (either internal or external) and wait for answer

- Press interactive button below where display says “more” (last key under display)

- Press button below where display says “conf” (first key under display)

- Make next call (either internal or external)

- When call is answered, press button below “add” (first key under display)

- Either make another call and press “add” key again or

- Press “add” key and then press “begin” key to commence conference.